Agrino 系統規格書
V1.1-Draft

Weather Board
Main Board
LPWAN Board
UART

UART

致謝
感謝下列的伙伴讓這個開源專案得以進展到現在.

Kobe Yu – Open Hack Farm
陳幸延 - Open Hack Farm
Shaw Wu - AgriWeather
Victor Sue - Pegatron
YK - NTHU
王祥恒 – NTU
Ray Tai– Might
Antony – LaBest
Owen – LaBest
Jimmy - LaBest
王英傑 - 公信電子

飲水思源 特別感謝

修訂歷史

日期	修訂內容	作者	備註
20171001	初版	Kobe Yu
20171129	新增: / - 致謝/系統總覽 / 異動: / - 系統方塊圖 / 刪除: / - V1.0	Kobe Yu
20171218	新增: / - Arduino nano / - LDO to wb / - GPIO to connector / 刪除: / - 土壤感測器接腳	Kobe Yu
20171225	新增: / - WB Pin Define / - MB RTC INT Define	Kobe Yu

一.系統總覽
    此系統總共包含3個模組分別是:
1. Weather Board
  主要功能透過版子上的MCU透過I2C/HW INT/Analog pin擷取大氣環境感測資料,包含了空氣溫溼度,氣壓,光強度,光輻射,風速風向跟雨量.
2. Main Board
  有3個主要功能:
  1. 擷取感測器資料,土壤感測器(RS485),Weather Baord(tx/rx)...etc
  2. 電源管理,偵測目前電池電量,
  3. 資料傳輸(實現通訊協定)
3. LPWAN Board
  此為外接模組,主要提供無線通訊功能,可能的模組與無線網路為:
  1. Long Distance(>1Km): LoRa/Sigfox/NB-IOT
  2. Short Distance (>100m):Wifi/Zigbee/BLE

二.Weather Board
Description...
1.系統方塊圖

​​ATSAMD21G18A-AU
(Arduino M0)
太陽輻射
BPW21
SHT31
大氣溫溼度
日照量
BH1603
風速
風向
雨量
Power From MainBoard

LDO
Power From USB

3v3

Analog

Analog

I2C

    HW INT

    Analog

    HW INT

TxRx to Main Board

2.Pin Define
Component	Item No	Type	M0 Pin	D21 Pin
日照量	BH1603(Data)	Analog	A4	PA05
日照量	BH1603(GC1)	Digital		PA02
日照量	BH1603(GC2)	Digital		PA04
太陽輻射	BPW21	Analog	A5	PB02
大氣溫溼度	SHT31	I2C	D20/D21	PA22/PA23
大氣溫溼度	SHT31(Alarm)	Digital(Alarm)		PA16
大氣溫溼度	SHT31(Reset)	Digital		PA17
風速	APRS(SEN0186)	HW INT	D9	PA07
風向	APRS(SEN0186)	Analog	D8	PA06
雨量	APRS(SEN0186)	HW INT	D7	PA21
MB	To MB	TX(to MB)		PA10
MB	To MB	RX(to WB)		PA11
LDO	Sensor PWR EN	Digital		PB11

三.Main Board
Description...
1.系統方塊圖

LDO

Power from Battery

Power from USB

3v3
(system)

Li-Polymer
Charger
Power from
solar panel

To Battery

Main Chip
Arduino Pro mini
MT7688
MTDuino
Weather Board(tx/rx)

LPWAN Board(tx/rx)

RTC
SD
Card
SPI

I2C

INT

D2
D3

LDO

Power from Battery

Power from USB

3v3
(sensors)

LDO

Power from Battery

Power from USB

3v3
(weather board)

2.Pin Define
System	Description	Arduino Pro mini	MTDuino	MT7688 Duo	Arduino Nano
Solar_v	Detect solar voltage	A0	A0	A0	A0
Battery_v	Detect battery voltage	A1	A1	A1	A1
WB_Tx/Rx	Communication between WB and MB	D0/D1	D0/D1	D0/D1	D0/D1
RF_Tx/Rx	Communication between Wireless module and MB	D6/D7	D6/D7	D8/D9	D6/D7
SDCard	Local storage	SPI(D14~D17)	SPI(D10~D13)	-	SPI(D14~D17)
LDO(sensor)	Control Power to sensors	D4	D4	D4	D4
LDO(wb)	Control Power to weather board	D5	D5	D5	D5
RTC INT	Trigger MCU INT	D3(INT1)	D3(INT9)	INT11(INT)	D2(INT0)
Connector / (註1)	GPIO to connector	D8/D9/D10/A2/ / A3	D8/D9/D10/A2/A3	D8/D9/D10/A2/A3	D8/D9/D10/A2/ / A3

四.備註
註1 - connector 樣式(可用螺絲鎖緊的 https://www.indiamart.com/proddetail/pcb-connector-10732221755.html)